## Slide 1: Stream Response to Precipitation Event
Hydrology Lab
Posted by Irina Overeem, May 2016

## Slide 2: Hydrological Watershed
Watershed or drainage basin
Topographical area that contributes all the water that passes through a given cross-section of a stream or river
(after Dingman, 2008)

## Slide 3: Conservation of Mass
Law of Conservation of Mass
Mass is neither created nor destroyed, for a given control volume and a defined time span.
Amount In – Amount Out = Storage
I – Q = ΔS
or, rate of inflow minus rate of outflow equals the rate of change in storage:
I/Δt – Q/Δt = ΔS/Δt
Recall this can be written at instantaneous rate:
i-q=dS/dt
Rainfall rate i
Qutflow rate q

## Slide 4: Experimental watershed in Iowa, Treynor watershed
Digital Elevation Model in TOPOFLOW, 30m x,y resolution, 870m by 1320 m
site_DEM.rtg and site.rti (and the other input grids).
Treynor Watershed
Very small Agricultural Research Watershed in the Corn Belt in Iowa. Consist of deep loess soils, and is mostly single-cropped. Has been a study watershed for many decades for rain, runoff and erosion observations.

## Slide 5: Theoretical Precipitation Input
Constant Rain Rate = 54 mm/hr for 3 hrs.
Stepwise Rain Rate = 156 mm/hr for 1 hr
Chart: Theoretical rain storms, 155 mm of rain total

## Slide 6: Real-world Precipitation Input
Input file: 00_June_20_67_rain_rates.txt
The rain rates values are listed every minute for 180 minutes
Chart: Treynor watershed rain storm, June 1967, totals 155 mm
A graph showing water input over time is called a “hyetograph”

## Slide 7: Stream Response Concepts
1
2
A graph showing water discharge over time is called a “hydrograph”
WMT Output file: basin-outlet-water-xsection_volume flow rate
More upstream in a catchment the hydrograph shows a higher peak and
more rapid response to a rainfall event
2. Further downstream, the contributing are is larger and response is more dampened.

## Slide 8: Hydrograph Treynor, 3hr constant rain rate

## Slide 9: Spatial distribution of Discharge Treynor, 3hr constant rain rate

## Slide 10: Hydrograph Treynor, 3hr variable rain rate

## Slide 11: Questions with Model Experiments
Calculate whether mass is conserved? Compare the rainfall influx and discharge outflux.
Why are these results unrealistic? Discuss missing processes, develop a hypothesis on how these processes impact water outflux.
What watershed parameters are set to be spatially uniform that are likely non-uniform?

## Slide 12: References
Dingman, S.L., 2008. Physical Hydrology, 2nd edition. ISBN 987-1-57766-561-8.
Onstad, C.A., Piest, R.F., Saxton, K.E. 1976. Watershed Erosion Model Validation for Southwest Iowa. Proceedings of the Third Federal Interagency Sedimentation Conference, March 1976.

## Slide 13: References
Dingman, S.L., 2008. Physical Hydrology, 2nd edition. ISBN 987-1-57766-561-8.
Onstad, C.A., Piest, R.F., Saxton, K.E. 1976. Watershed Erosion Model Validation for Southwest Iowa. Proceedings of the Third Federal Interagency Sedimentation Conference, March 1976.