## Slide 1: EF5: A hydrologic model for prediction, reanalysis and capacity building
Zachary Flamig
Postdoctoral Scholar

## Slide 2: Ensemble Framework for Flash Flood Forecasting
Evapotranspiration
Native data options:
1. GeoTIFF PET
2. GeoTIFF temperatures
Precipitation
Native data options:
1. MRMS
2. GPM/TMPA RT
3. Any GeoTIFF
  QPE
  QPF
Surface Runoff
Simulation options:
1. CREST
2. SAC-SMA
3. Hydrophobic
Snowmelt
Simulation options:
1. SNOW-17
Routing
Simulation options:
1. Linear reservoir
2. Kinematic wave
Outputs
Type options:
1. Streamflow
2. Recurrence interval
3. Water depth
4. Soil moisture
Parameter Optimization
Type options:
1. DREAM
Inputs
Model
Outputs
Inundation
Simulation options:
1. Mass conservation
Flamig, Z. L., H. Vergara, R. Clark III, Y. Hong, and J. J. Gourley, 2016: EF5: Version 1.0. doi: 10.5281/zenodo.59123

## Slide 3: Ensemble Framework for Flash Flood Forecasting
C++
19,815 Lines of code
1,189 Total water balance (6%)
919 Total routing (5%)
89% “Glue” code!
  Configuration
  I/O

## Slide 4
Multi-Radar Multi-Sensor QPE (MRMS)
Flooded Locations And Simulated Hydrographs (FLASH)
MRMS/Q3 Rainfall Observations
1km2/2 min
Stormscale Distributed Hydrologic Model Framework
-1km2/10 min
10-11 June 2010, Albert Pike Rec Area, Arkansas
250 mm/10”
200
150
20 fatalities
Flooding Impacts
Simulated surface water flows and return period
Probabilistic Forecast Products on the Flash Flood Impacts and Magnitudes (70% chance of hazardous road flooding)
First distributed hydrologic modeling framework to operate at the flash flood scale in real-time across the conterminous USA

## Slide 5: Comparison with National Water Model
NWM
  2.6 million forecast points
  Single physics solution
  Calibrated
FLASH
  10.2 million forecast points
  Multiple water balance physics
  A priori parameters

## Slide 6: Comparison with National Water Model
Forecast time (Valid Time)
Initialization Time
00:00
00:00
00:10
00:20
00:30
00:40
00:50
01:00
01:00
12:00
18:00
FLASH
NWM

## Slide 7: Hydrologic Reanalysis
EF5 with CREST/SAC-SMA/HP & Kinematic Wave Routing
  Apriori parameters
  0.01x0.01˚ spatial resolution over CONUS
  5-minute time steps
  MRMS precipitation rate as forcing
Kept daily values
  Maximum Q
  Time of maximum Q
  Maximum unit Q
  Minimum soil moisture
Kept complete basin outlet time series for gauged basins <1000 km2
2002-2011 period of record for MRMS forcing
  2001 used as warmup period

## Slide 8
Observed and simulated hydrographs from Caddo River near Caddo Gap, AR. The contributing basin area at this point is 352 km2.

## Slide 9
Observed and simulated hydrographs from Little Missouri River near Langley, AR. The contributing basin area at this point is 177 km2.

## Slide 10: Simulation Validation
CREST water balance
4,366 USGS gauges

## Slide 11: Simulation Validation
CREST water balance
4,366 USGS gauges

## Slide 12
http://flash.ou.edu/reanalysis
Reanalysis
Produced daily from 2002-2011:
Maximum Streamflow
Maximum Unit Streamflow
Time of day of Maximum Streamflow
Minimum Soil Moisture

## Slide 13: EF5 Capacity Building
Windhoek, Namibia 2015
Puebla, Mexico 2015
Villahermosa, Mexico 2015
Windhoek, Namibia 2016
Nairobi, Kenya 2017

## Slide 14: http://ef5.ou.edu
Reanalysis
http://flash.ou.edu/reanalysis
Produced daily from 2002-2011:
Maximum Streamflow
Maximum Unit Streamflow
Time of day of Maximum Streamflow
Minimum Soil Moisture
http://ef5.ou.edu/videos