## Slide 1
James PM Syvitski
CSDMS Integration Facility, U. Colorado—Boulder
Satellite Sensing of Deltas
Syvitski, Kiel Short Course 2013
Presentation will focus on SRTM, AMSR-E, InSAR, MODIS, high-res optical, TRMM, GRACE and NIR, and cover such delta topics as DEM vs. DTM, hydrology (stage height, flow velocity, river width & depth, SSC, precipitation, evapotranspiration, soil moisture, groundwater), flood inundation

## Slide 2
Match orbital sensor with objective, considering resolution, repeat interval, wavelengths, post-processing methods.
Consider timing: river stage, tidal stage, storm surge stage, seasonal effects, vegetation vs. water vs. turbidity; cloud cover and other atmospheric moisture
Syvitski, Kiel Short Course 2013

## Slide 3
DEM Outline:
SRTM Mission
SRTM Data Resolution
SRTM Data Issues
Floodplains and Deltas
Historical Maps vs SRTM data
Syvitski, Kiel Short Course 2013

## Slide 4
SRTM Mission
Joint project of the National Geospatial-Intelligence Agency (NGA), NASA, German & Italian Space Agencies
Interferometric synthetic aperture radar (InSAR) survey during an 11-day shuttle mission to collect high-res digital elevation data for 80% of the Earth landmass (60N - 59°S)
C-band and X-band data collected: C band monitored 99.96% of the targeted landmass at least once, 94.59% at least twice, and ~50% three or more times
Syvitski, Kiel Short Course 2013

## Slide 5
SRTM Data Resolution
The vertical resolution depends on location, terrain characteristics and surface feature properties.
Reported elevation RMSE (m) for the SRTM DEM
16 Mission specification
6.5 (Rodriguez et al., 2005)
6 Haase and Frotscher (2005)
5.5 LeFavour and Alsdorf (2005)
4.1 Gorokhovich and Voustianiouk (2006)
3.7 Berry et al. (2007): near global relative vertical accuracy
1.1–1.7 Schumann et al., in press: for the world’s flat-lying areas
Syvitski, Kiel Short Course 2013

## Slide 6
SRTM Data Resolution — A horizontal pixel is 1-arc or 3-arc seconds
Difference between 30m & 90m horizontal resolution, Mississippi floodplain
Syvitski, Kiel Short Course 2013

## Slide 7
SRTM Data Resolution
A horizontal pixel is 1-arc or 3-arc seconds, depending on data availability
30 m horizontal resolution
Mississippi floodplain detail
90 m horizontal resolution
Syvitski, Kiel Short Course 2013

## Slide 8
SRTM Data Issues
“Finished” SRTM data has voids filled in, terrain data edited with a vector shoreline database (SRTM Water Body Data Set) to depict coastlines & shorelines, and rivers.
SRTM DEM consists of static heights over land, and tidally adjusted TOPEX/Poseidon–derived ocean heights, to accommodate tidal variations during the mission
Ocean elevation was set to 0 m, lakes of 600 m or more in length were flattened to a constant height, and rivers that exceeded 183 m in width were delineated and monotonically stepped down in height
The finished product is a uniform grid of elevation values indexed to specific points on the ground in a standardized Digital Terrain Elevation Data (DTED®) format.
Other issues: canopy, snow, and desert sand versus the earth surface
unfinished
finished
Syvitski, Kiel Short Course 2013

## Slide 9
To overcome the speckling associated with canopy, it is necessary to reduce the vertical resolution from 1 to 2 m. Shuttle Lidar (SLA-02) may be used to determine canopy height and ground elevation and to adjust SRTM bands.
Amazon Delta with its jungle cover
Each color represents 1 m in elevation
Each color represents 2 m in elevation
Syvitski, Kiel Short Course 2013

## Slide 10
To overcome the specking associated with dunes, it is necessary to reduce the vertical resolution from 1 to 3m or even 5m; e.g. Murray/Darling Aust.
Each color represents 1 m in elevation
Each color represents 3 m in elevation
Each color represents 5 m in elevation
Syvitski, Kiel Short Course 2013

## Slide 11
Pearl altimetry, purple <0m, lt blue 0m, brown 0-2m, dk yellow 2-3m, lt green 3-4m, yellow 4-5m, dk green 5-35m, dk brown 35-65m, dk blue 65-95m, black >95m.
Syvitski, Kiel Short Course 2013

## Slide 12
Po altimetry binned at 1 color per 1 m vertical intervals; colors cycled every 10 m, to a height of 100 m, then black; sea level light blue, below mean sea level - shades of pink.
Syvitski, Kiel Short Course 2013

## Slide 13
Pink areas are below sea level
Nile
Ganges
Mississippi
Mekong
Euphrates
Yellow
Indus
Mahakam
Vistula

## Slide 14
1829
1833
1847
1856
1861
1872
1875
1897
1922
Syvitski, Kiel Short Course 2013

## Slide 15
2000 SRTM image
Elevations in 1 m bins
Krishna
Godavari
Black: 1922
Brown: 1872
Red: Letts
Blue: 1832
Green: 1832
90 m
C-band
Syvitski, Kiel Short Course 2013

## Slide 16
Indus River & Floodplain
Syvitski, Kiel Short Course 2013

## Slide 17: Ocean Surge Mapping (cyclone, tsunamis)
SRTM 90m topographic data overlay with MODIS flood extend map in red.
Cyclone Nargis, Irrawaddy Delta with MODIS Terra, May 5th, 2008.
Floods are widespread, 85% of the studied deltas experienced flooding.
From 2001-2008, in the 33 deltas ~260,000 km2 was submerged by floods.
Syvitski, Kiel Short Course 2013
Notes: Accuweather.com, Cyclone Nargis made landfall with sustained winds of 130 mph and gusts of 150-160 mph, which is the equivalent of a strong Category 3 or minimal Category 4 hurricane. This is a much larger area then

## Slide 18
100 km
11-day (237-248) sequence of MODIS satellite images (either Terra or Aqua) showing the 2nd major levee breach of the 2010 Indus River flood.
Syvitski, Kiel Short Course 2013

## Slide 19
Indus
Pakistan
Phet
Syvitski, Kiel Short Course 2013

## Slide 20
Mekong
SRTM: morphology & surface elevation
NIR: Surface water as black or shades of blue depending on the sediment concentration
Vis: Water turbidity
MODIS: Dartmouth Flood Observatory (CSDMS) mapping
DFO
SRTM
NIR
Vis
Syvitski, Kiel Short Course 2013

## Slide 21
 | Delta area (km2) |  | 
Delta | <0 | <1 | <2
Brahmani | 40 | 207 | 640
Chao Phraya | 263 | 734 | 1775
Ganges B | 1988 | 3682 | 6173
Indus | 1213 | 2558 | 4753
Irrawaddy | 40 | 265 | 1104
Mekong | 7156 | 13621 | 20908
Mississippi | 1876 | 4258 | 7142
Nile | 5051 | 7212 | 9435
Orinoco | 197 | 629 | 1801
Parana | 245 | 1262 | 3597
Pearl | 2499 | 3163 | 3719
Po | 602 | 622 | 633
Rhone | 752 | 1007 | 1144
Tigris | 2297 | 5130 | 9711
Vistula | 1221 | 1376 | 1488
Yangtze | 2206 | 3896 | 7084
Yellow | 1235 | 2253 | 3424
Total area | 29387 | 53032 | 87534
Syvitski, Kiel Short Course 2013

## Slide 22: METHODS: how InSAR works
Sun (2008)
Syvitski, Kiel Short Course 2013

## Slide 23: advantages of InSAR
High spatial resolution (~20m horizontal and ~1 cm vertical)
Long time range (10-20 years)
Inexpensive
Free of data sharing, land access problems
GPS stations
Stratigraphy
Tide gauges
Leveling surveys
Extensometers
Syvitski, Kiel Short Course 2013
Higgins et al., 2013

## Slide 24: Suitable data for interferometry
Syvitski, Kiel Short Course 2013
Higgins et al., 2013

## Slide 25: Selecting SAR scenes
Small spatial baseline
Correct temporal baseline
Orbital geometry that reduces shadowing, layover and foreshortening
DEM availability
Best atmospheric conditions
Cost and accessibility
Reliable orbital information
Largest available date range
Baseline
E.S.A. Basic Radar Course
Syvitski, Kiel Short Course 2013

## Slide 26: InSAR…
Syvitski, Kiel Short Course 2013
Higgins et al., 2013

## Slide 27
Dec 2008 – Feb 2009
Dec 2010 – Feb 2011
Dec 2009 – Feb 2010
36 km
+3 cm
0 cm
-3 cm
Syvitski, Kiel Short Course 2013

## Slide 28: shows RELATIVE ground deformation in 46 days
3 cm +C
0 cm +C
-3 cm +C
Syvitski, Kiel Short Course 2013
Higgins et al., 2013
Notes: Here is an interferogram from the starred box.
It has been corrected for TOPOGRAPHY and for ORBITAL ERRORS (orbital drift + the satellite is wrong about where it is in the sky)
It has NOT been calibrated with a GPS yet. That means that these numbers are RELATIVE. You can think of it as a deformation pattern riding ON TOP OF the bigger-footprint signal that Mike observed.
That’s where the GPS comes in.
PS… if these #s seems extreme to ppl… show the spread in the GPS data (2cm within a couple of days).

## Slide 29: We can change from RELATIVE to ABSOLUTE by using a GPS station. The 2nd station then gives an estimate of error. … one point, 2 mm
RPUR
DHAK
+3.0116 cm
0.116 cm
-2.8840 cm
Syvitski, Kiel Short Course 2013
Higgins et al., 2013
Notes: I did a five-day average around the GPS point for the days of each frame. I subtracted them to get the estimate.
I did a 25-pixel box around the locations to get a phase over the InSAR pixel for each station. The method is still rough though. I basically overlay in google earth to find the right pixel. That needs to improve. The box size is also arbitrary.
BUT early results on two shows agreement of about 1-2 mms.
Harass them: I need the later GPS data plz! :0)

## Slide 30
Advanced methods like D-InSAR or PS-InSAR isolate the varied ways humans impact the earth’s surface
- Higgins et al., 2013
17m spatial pixel
~1 to 2mm vertical resolution
1 m subsidence in 4 yr
Syvitski, Kiel Short Course 2013

## Slide 31
From Higgins et al. (2013)
Fish ponds
Down 200 mm
Down 200 mm
Down 90 mm
Down 120 mm
Down 90 mm
Syvitski, Kiel Short Course 2013

## Slide 32
Syvitski, INQUA/IGCP Kiel, 2012
Advanced methods like InSAR can help isolate the varied ways humans impact the earth’s surface

## Slide 33
Mekong
Syvitski, Kiel Short Course 2013
Visible bands are the most popular satellite wavelength. It is what we would see from an airplane. Can be used to trace vegetation, SSC, etc

## Slide 34
250 m
2001
2008
Syvitski, Kiel Short Course 2013

## Slide 39
Reservoirs cause more than 2.3 Gt/y less sediment to reach the coast worldwide
2003

## Slide 40
Stage Height: larger rivers, reservoirs using LIDAR or RADAR Altimetry
ICESAT-II & GLAS (Geoscience Laser Altimeter System) 70m “spots” at steps of 170m)
OSTM/Jason 2 (RADAR Altimetry 10cm rms, 100m wide, weekly) could get surface slope to calculate flow velocity
Syvitski, Kiel Short Course 2013

## Slide 41
Stage Height: larger rivers, reservoirs using LIDAR or RADAR Altimetry
Advantages: Day/night, all weather. Unhindered by canopy. Heights within a common reference frame. Repeat orbits enabling systematic monitoring: rivers, lakes, wetlands, inland seas and floodplains. Offers information to traditional or absent gauge (stage) data. Past to future missions allow for seasonal to inter-annual variations. Techniques validated.
Limitations: Retrieved heights are an "average" of all topography within the footprint. Differs from traditional gauge measurements which offer "spot" heights at specific locations. Altimeters only retrieve heights along a narrow swath with instrument's footprint, that can vary up from 100’s m. Target size is controlled by size of instrument footprint, telemetry/data rates, surrounding topography and target-tracking method used. Improved temporal coverage is gained at the expense of spatial coverage for a single satellite mission.
Syvitski, Kiel Short Course 2013

## Slide 42
Stage Height: larger rivers, reservoirs using LIDAR or RADAR Altimetry
SRTM Mission Interferometric synthetic aperture radar (InSAR) survey during an 11-day shuttle mission collected high-res digital elevation data for 80% of the Earth landmass (60N - 59°S): C band monitored 99.96% of the targeted landmass at least once, 94.59% at least twice, and ~50% three or more times
SRTM Water Body Data Set --- rivers that exceeded 183 m in width were delineated and monotonically stepped down in height
Syvitski, Kiel Short Course 2013

## Slide 43
River Width: medium to large rivers
AMSR-E: Advanced Microwave Scanning Radiometer-EOS
Spatial Resolution: ≈25 km at 32.5 GHz
Uses the ratio of horizontal polarized radiance from measurement site and comparison site pixels as a proxy for flow area and river width
As rivers rise, flow width and within-reach water area increases.
In contrast to gauging stations located at river sections where discharge change is accompanied mainly by water level changes, AMSR-E sites are located where discharge change is accompanied by significant changes in water surface area.
The calibrated AMSR-E signal is used as a discharge estimator.
AMSR-E pixel
Syvitski, Kiel Short Course 2013

## Slide 44
For high latitude rivers (e.g. Lena River), the summer is characterized by measurement site brightness temperatures that are much lower than at the nearby calibration pixel (because of the surface water area provided by the open river. Discharge variation during this season is sensitively tracked by the upwelling microwave radiance and converted via an initial rating equation to discharge values, with constant discharge for sub-ice conditions.
When the river freezes in the fall, the relative measurement and calibration brightness temperatures are reversed. Spring ice thaw and breakup are preceded by synchronous rises in radiance values; in May, with river ice removal, the measurement pixel value drops very sharply as the spring flood commences.
Syvitski, Kiel Short Course 2013

## Slide 45
AMSR-E estimated river discharge

## Slide 46
River Depth: shallow rivers, reservoirs
Sensor with a green band ≈550 µm --- can see through clear water up to 25m e.g. LANDSAT, ASTER, ENVISAT, MODIS etc
Measures the return radiance at calibration stations. Relationship used to map depth between calibrated stations.
Both ASTER (Advanced Spaceborne Thermal Emission and Reflection Radiometer) on the Terra Satellite and LANDSAT offer a footprint size of 15 to 30 m.
Syvitski, Kiel Short Course 2013

## Slide 47
Precipitation: Near global to global using radars and radiometers
TRMM or Tropical Rainfall Measuring Mission provides near real time precip estimates every 3 hrs at 0.25° x 0.25° using Precipitation Radar, TMI Passive Microwave Radiometer (10.7 to 85.5 GHz), VRS Visible & Infrared Scanner. TRMM precip data (since 1998) is combined with SSM/I data (0.5° x 0.5°, since 1997), low-orbit GOES IR (1°x1°, 3-hourly), TIROS Operational Vertical Sounder (1°x1°, daily), the Advanced Microwave Scanning Radiometer - EOS (AMSR-E), the Advanced Microwave Sounding Unit (AMSU-B), and gridded rain gauge data run through algorithm 3B-43.
Syvitski, Kiel Short Course 2013

## Slide 48
Evapotranspiration estimates, 2000-2006, every 8 days; 0.05° x 0.05° grid) from MODIS ET16 algorith.
Evaporation: Global
Evapotranspiration estimates are from the MODIS ET (MOD16) algorithm developed by Mu et al. (2007), based on the Penman-Monteith equation, modified with satellite information that: (1) adds vapor pressure deficit and minimum air temperature constraints on stomatal conductance; (2) uses leaf area index as a scalar for estimating canopy conductance; (3) replaces the NDV Index with the Enhanced Vegetation Index; and (4) adds a calculation of soil evaporation.
Syvitski, Kiel Short Course 2013

## Slide 49
Soil Moisture: ASAR imaging microwave radar (30m × 30m), RADARSAT-1 & PALSAR (6.25m × 6.25m)
ASAR: Niger
Syvitski, Kiel Short Course 2013

## Slide 50
Groundwater: GRACE (Gravity Recovery And Climate Experiment)
“Tom” and “Jerry” each fly about 220 km apart, microwave band keeps track of distance between the two—picks up changes in the geoid (sensitive up to 10 µm)
Syvitski, Kiel Short Course 2013

## Slide 51
Suspended Sediment Concentration: medium to large rivers, reservoirs
MODIS, LANDSAT, ENVISAT, OCEANSAT, ASTER
MODIS (Moderate Resolution Imaging Spectroradiometer) 2 bands at 250 m pixel; 5 bands at 500 m pixel; 29 bands at 1 km pixel),
LANDSAT (8 Spectral bands, pixel 15 to 30 m, 0.45 to 12.5 μm),
ENVISAT (MERIS),
OCEANSAT (8 spectral bands visible to nearIR, 360m res)
(From McGrath & Overeem 2010 and Hudson et al (2013))
Band 1 = 620-670nm
PL
Q
SM
MODIS Band1 Reflectance maps Plume Length: ρ(λ) ~ a PL
Plume Length is a function of River Discharge: PL ~ b Q
River Discharge is function of Surface Melt (SM): SM ~ c Q
Syvitski, Kiel Short Course 2013

## Slide 52: MODIS Plume Length vs Discharge
Syvitski, Kiel Short Course 2013
(From McGrath & Overeem 2010

## Slide 53: GRACE data vs Plume timing
Data courtesy: Ursula Rick, Waleed Abdalati & Jason Box.
Syvitski, Kiel Short Course 2013