## Slide 1: RUNNING A STAND-ALONE MODEL Climate-hydrological modeling of sediment supply
Run & Couple Surface Dynamics Models
Run & Couple Surface Dynamics Models

## Slide 2: Outline
  OBJECTIVE
  Learn How to Run a Model in the CMT
  EDUCATIONAL EXAMPLE HYDROTREND
  Why is sediment supply important? Delta formation
  Quantifying Sediment Supply Processes
  Simple Scenario and User Changes to Input Parameters
  HANDS-ON
  Run a climate change scenario and human impacts scenario for 21st century

## Slide 3: Why Model Sediment Supply?
Worldwide 500 million people live in low-lying deltas
Thirty-three major deltas combined have >100,000 km2 at elevation < 2m a.s.l.
(Syvitski et al., 2009).
Sediment affects River Deltas Elevation (ΔRSL) by Aggradation (A)
Mississippi Delta, USA
Ganges-Brahmaputra Delta, India & BD
Notes: Accuweather.com, Cyclone Nargis made landfall with sustained winds of 130 mph and gusts of 150-160 mph, which is the equivalent of a strong Category 3 or minimal Category 4 hurricane. WRF runs

## Slide 4: Aggradation due to Floods in Deltas
SRTM 90m topographic data overlay with MODIS flood extend map in red.
Cyclone Nargis, Irrawaddy Delta
MODIS Terra, May 5th, 2008.
Floods are widespread, 85% of 33 studied deltas experienced flooding (2001-2008). Total of ~260,000 km2 was submerged by floods.
Question: are changes in precipitation regimes changing floods into 21st century?
Notes: Accuweather.com, Cyclone Nargis made landfall with sustained winds of 130 mph and gusts of 150-160 mph, which is the equivalent of a strong Category 3 or minimal Category 4 hurricane. WRF runs

## Slide 5: Reduced Aggradation due to Damming
1.4 ± 0.3 billion tons per year LESS sediment reaches the coast worldwide.
Question: how is a new planned dam influencing the sediment flux at the coast?

## Slide 6
Ok. It’s important. But how do we quantify sediment supply for an arbitrary river?

## Slide 7: Numerical Model HydroTrend
Critical Dynamic Boundaries: Rain-Snow-Ice
Daily temperature combined with hypsometry and lapse-rate determine the freezing line altitude (FLA) and thus the parts of the basin that get rained on or snowed on.
Glacier equilibrium line altitude (ELA) combined with the hypsometric curve determines the area of the basin covered with glaciers, and thus area contributing to ice accumulation and ice melt.

## Slide 8: Suspended sediment flux
Qs sediment load MT/yr
ω 0.0006
Q discharge in km3/yr
A drainage area in km2
R relief in km
T mean annual basin-wide temperature in deg C
The regression for this model is based on analysis of a global database of last century discharge and sediment load observed at river mouths of 100’s of rivers (Syvitski & Milliman, Journal of Geology, 2007).
For T-annual >= 2deg C

## Slide 9
The model simulates Trapping Efficiency, TE, based on the modified Brune equation (Vörösmarty et al., 1997), for reservoirs volumes, V, larger than 0.5 km3
Trapping sediment in lakes or reservoirs in HydroTrend
Wherein ∆τ is the approximated residence time and Qj is the discharge at mouth of each subbasin j (m3 s-1) draining to a specific lake:
Notes: The trapping acts on the sediment pulse generated
NOT TAKEN INTO ACCOUNT IN FIRST RUNS

## Slide 10: HydroTrend Hands-On Notes
Activate your VPN for secure connection
Make sure you have Java 1.6
Launch the CMT tool (from the CSDMS website)
Log in to beach.colorado.edu
Open Group: Coastal
Open Project: Hydrotrend + Avulsion +CEM
Drag in HydroTrend Component to be the Driver
Change Settings in the HydroTrend Configure Menu
Run Simulations, Look at your results in the Console
5 Minutes
10 Minutes

## Slide 11: River response to climate change?
What is the effect of a 100% increase of precipitation over the next century?
HydroTrend Configure Menu: adapt precipitation

## Slide 12
The ‘Help’ button in the Configure Menu links to online information on model parameters.

## Slide 13: River system response to human impacts?
Model a planned drinking water supply reservoir in the basin. The reservoir would have 1800 km2 of contributing drainage area, and be 1 km long and 100m wide, 5m deep.
HydroTrend Configure Menu: adapt reservoir settings

## Slide 14: Output
Daily Sediment Load Output
base-case
reservoir
Daily Water Discharge Output
base-case
precipitation
Drastic changes in water flux result from increased precipitation regime,
Drastic reduction in sediment flux results from damming.

## Slide 15: Educational Material in CSDMS wiki
http://csdms.colorado.edu/wiki/Labs_portal
http://csdms.colorado.edu/wiki/Lectures_portal

## Slide 16: References
Syvitski, J.P.M., Kettner, A.J., Hannon, M. T., Hutton, E.W.H., Overeem, I., Brakenridge, G.R., John Day, J., Vörösmarty, C., Saito, Y., Giosan, L., Nicholls, R.J., 2009. Sinking Deltas due to Human Activities. Nature Geoscience, 2, 681 - 686.
Kettner, A.J., and Syvitski, J.P.M., 2008. HydroTrend version 3.0: a Climate-Driven Hydrological Transport Model that Simulates Discharge and Sediment Load leaving a River System. Computers & Geosciences, 34(10), 1170-1183.