## Slide 1: COUPLED MODELING River – Delta Plain to Longshore Transport Irina Overeem (with help of Andrew Ashton and Eric Hutton)

## Slide 2: Outline
  OBJECTIVE
  Learn How to Run Coupled Components in the CMT
  Discuss science & technology challenges associated with coupling.
  EXAMPLE : AVULSION-CEM
  River Changes affecting Coastline Evolution Processes
  Simple Scenario and Changes to Input Parameters
  LAB 4
  Set up a coupled run for two distributary channels
  feeding ‘wave-dominated’ deltas.

## Slide 3: HYDROTREND Component
Task: to deliver water, sediment load from an entire drainage basin to a delta apex.
Needs: climate and basin characteristics
Provides: Q, Qs, Qb at delta apex

## Slide 4: Avulsion Component
Task: to route the distributary channel(s) from the delta apex to the coastline
Needs: incoming water and sediment flux, number of dist. channels and specifications for switching frequency
Provides: sediment flux for 1 – 5 river mouths at coastline

## Slide 5: Avulsion Component
Task: to route the distributary channel(s) from the delta apex to the coastline
Needs: incoming water and sediment flux, number of dist. channels and specifications for switching frequency
Provides: sediment flux for 1 – 5 river mouths at coastline

## Slide 6: Coastline Evolution Model
Task: to evolve a shoreline due to gradients in breaking-wave-driven alongshore sediment transport.
Needs: incoming sediment flux at coast, wave regime
Provides: offshore deposition and erosion (elevation)

## Slide 7: Coastline Evolution Model Some Theory…….. 1. What is wave-dominated delta? 2. Basic mechanism of longshore transport.

## Slide 8: Wave-influenced Deltas
river
tides
waves
Galloway, 1975
Arno River Delta, Italy
Rosetta Lobe, Nile Delta, Egypt

## Slide 9: Alongshore Sediment Transport
breaking-wave-driven alongshore sediment transport (within the surf zone) is highly dependent on wave angle
maximizing angle:
~45 degrees

## Slide 10: traditional approach
combining the conservation of mass:
with the small angle approximation
Qs = K Hb5/2 cos (fb - q) sin (fb - q )
Qs = K Hb5/2 (1) dy / dx
generates a shoreline evolution equation:
  (classic diffusion equation)

## Slide 11: low-angle waves

## Slide 12: high-angle waves

## Slide 13
angle-dependent shoreline diffusivity

## Slide 14
‘Coastline Evolution Model’
discretizes the plan-view domain
tracks one contour line – the shoreline
simple wave refraction
Ashton and Murray, JGR-ES 2006
numerical model: ‘CEM’

## Slide 15
random distribution of waves selected from PDF
controlled by:
    U = proportion of high-angle, ‘unstable’ waves
    A = asymmetry (proportion of waves approaching from left, driving alongshore sediment transport to the right)
waves from all angles

## Slide 16
simulated low-angle spits

## Slide 17
simulated low-angle spits

## Slide 18
simulated low-angle spits

## Slide 19
CEM results- symmetrical waves

## Slide 20: Symmetrical wave-influenced deltas
Rosetta Lobe, Nile Delta, Egypt
Arno River Delta, Italy
Bhattacharya & Giosan, 2002

## Slide 21: asymmetrical wave-influenced deltas
Damietta Lobe, Nile Delta, Egypt
Bhattacharya & Giosan, 2002
Danube Delta, Romania

## Slide 22
delta morphologies with asymmetry

## Slide 23
hypothesis test – Nile Delta
MedAtlas
hindcast
wave “energy”
(H012/5)

## Slide 24: two-way coupling through CMT
flexible ‘avulsion’ component to implement different fluvial flux and routing schemes
    fixed direction (several rivers)
    migrating river
    geometric ‘bifurcation’ rules
    dynamic upstream avulsion
simple feedback:
  Qb = a Sb, where
  slope S ~ river length
  b > 1 (non-linear)
  just a first try!

## Slide 25: River-CEM LAB 5
Launch the WMT tool (from the CSDMS website)
Select CEM Component to be the Driver
Link the River Component, the Discharge Component, and the Waves Component
Set up a run by making changes in the parameter menus of each component

## Slide 26: Simulation Wiring
CEM needs AVULSION to set a switching delta channel transporting bedload for sediment delivery to the coast, it needs WAVES to drive longshore tranport, the avulsion component needs incoming river discharge (CONSTANT).

## Slide 27: Coastline Response to Wave Dynamics?
Set up wave angle regimes which systematically change the asymmetry of the incoming wave field (A), and the proportion of high angle waves (U)
(from Ashton et al. )

## Slide 28: Multiple Distributary Channels
Set the number of rivers to two distributary channels.
If you adjust the sediment exponent, the channel with the shortest route to the coast will receive a higher proportion bedload at the division.
Change number
of rivers

## Slide 29: References
Ashton A., Murray B.A. Arnault O. Formation of Coastline Features by Large-Scale Instabilities Induced by High-Angle Waves. Nature Magazine. Volume 414. 15 November 2001.
Ashton A.D., Murray A.B. High-Angle Wave Instability and Emergent Shoreline Shapes: 1. Wave Climate Analysis and Comparisons to Nature. Journal of Geophysical Research. Volume 111. 15 December 2006.
Ashton A.D., Murray A.B. High-Angle Wave Instability and Emergent Shoreline Shapes: 2. Wave Climate Analysis and Comparisons to Nature. Journal of Geophysical Research. Volume 111. 15 December 2006.
Overeem, I., Syvitski, J.P.M., Hutton, E.W.H., (2005). Three-dimensional numerical modeling of deltas. SEPM Spec. Issue, 83. ‘River Deltas: concepts, models and examples’. p.13-30.
Hutton, E.W.H, Syvitski, J.P.M., 2008. Sedflux 2.0: An advanced process-response model that generates three-dimensional stratigraphy . Computer & Geosciences, 34-10, 1319-1337.