## Slide 1
Tutorial on Large-Eddy Simulation
Senthil Radhakrishnan
University of California Santa Barbara

## Slide 2: Simulation methodologies
High
speed
Low
speed
Turbulent transport is due to the vortical motions (eddies).

## Slide 3: Simulation methodologies
Turbulent transport is due to the vortical motions (eddies).
Solution methodologies:
  Full description of all eddies  Direct Numerical Simulation (DNS)
  Expensive
High
speed
Low
speed

## Slide 4: Simulation methodologies
Turbulent transport is due to the vortical motions (eddies).
Solution methodologies:
  Full description of all eddies (DNS)
  Statistical description of all eddies  Reynolds (time or ensemble) averaged solution of the Navier-Stokes (RANS) equations
  Limited Accuracy
High
speed
Low
speed

## Slide 5: Simulation methodologies
Turbulent transport is due to the vortical motions (eddies).
Solution methodologies:
  Full description of all eddies (DNS)
  Statistical description of all eddies (RANS)
  Partial description of the eddies  Large-Eddy Simulation (LES)
High
speed
Low
speed

## Slide 6: Resolution requirements for LES
Velocity decomposed into large-scale (resolved) and subgrid-scale (unresolved) parts.
  The large scales (integral scale), which depend on the boundary conditions (i.e., are flow dependent) are computed.
  The small scales, which are more universal (less dependent on boundary conditions) are modelled.
  Large scales contribute most of the Reynolds stresses.
The grid size must be a fraction (1/20-1/40) of the integral scale


## Slide 7: Cost: LES of wall-bounded flows
Outer layer:
  Need 20-40 points in each direction to resolve an integral scale .
Outer layer: only scales of order  must be resolved.  Cost - Re 0.6
Integral scale 

## Slide 8: Cost: LES of wall-bounded flows
 Cost  Re 2.4
Inner layer: near-wall eddies must be resolved.
  Grid must scale in wall units
  Nx Ny Nz  Re 1.8
Near-wall eddies u

## Slide 9: Wall-layer modeled LES (WMLES)
Alternative for high-Re applications:
  Bypass the wall layer
  Model its effects in an average sense.

## Slide 10: Wall-layer modeled LES (WMLES)
Alternative for high-Re applications:
  Bypass the wall layer
  Model its effects in an average sense.
Assumptions:
  Grid is so coarse that it contains a very large () number of near-wall eddies.
  The time-step is much larger than the near-wall-eddy timescale.

## Slide 11: Wall-layer modeled LES (WMLES)
Alternative for high-Re applications:
  Bypass the wall layer
  Model its effects in an average sense.
Assumptions:
  Grid is so coarse that it contains a very large () number of near-wall eddies.
  The time-step is much larger than the near-wall-eddy timescale.
The average effect of the near-wall eddies on the momentum transport can be accounted through RANS-like models


## Slide 12: Cost: LES of wall-bounded flows
Piomelli (2008)

## Slide 13: Wall-layer modeled LES (WMLES)
Various techniques:
  Equilibrium stress layer
    Assume a velocity profile (logarithmic law)
    Given the outer-flow velocity , use the assumed profile to compute the wall stress

## Slide 14: Sub-grid stresses
Sub-grid stresses:
Eddy viscosity based model of sub-grid stresses:
Smagorinsky model:

## Slide 15: Sub-grid stresses
Smagorinsky model:
Length scale = filter width which is proportional to grid spacing
Constant model coefficient Cs does not work well.
Calculate coefficient (Cs) using Germano et al. (1991) dynamic method.

## Slide 16: Grid convergence
C.-H. Moeng, J.Dudhia, J. Klemp, and P. Sullivan (2007)
Planetary boundary layer simulation
Coarse grid spacing:
150m X150m X 20m
Fine grid spacing:
50m X 50m X 20m

## Slide 17: Grid convergence

## Slide 18: Channel flow: Synthetic turbulence at the LES inlet
Controlled
Keating and Piomelli (2004)

## Slide 19: Channel flow: Synthetic turbulence at the LES inlet
The flow rapidly loses turbulent kinetic energy and begins to relaminarize.
Eventually, the flow transitions and reaches acceptable turbulence levels 20downstream of the inflow.
Reference
Synthetic
Mean velocity
x/= 10
x/= 15
x/= 20

## Slide 20: Current status
TURBINS:
Suitable for low Reynolds number flows.
Can treat complex topography using immersed boundary method.
Linear solvers use PETSc’s library. Can handle non-uniform mesh in any direction.
DNS/LES code under development:
Suitable for high Reynolds number flows.
Can treat only flat terrain.
For performance reasons, it uses FFT based in-house direct linear solvers. However, it can treat non-uniform mesh along wall-normal direction only.
Development underway to add immersed boundary to treat complex topography, in-house iterative solvers to treat non-uniform mesh along any direction.