## Slide 1
Predictions of bedload transport in vegetated channels: uncertainties and steps forward
Elowyn Yager-University of Idaho
Collaborators: Mark Schmeeckle, Anne Lightbody, Alex Fremier
Notes: Start 7:02

## Slide 2
https://earthengine.google.org/#timelapse/v=-9.69993,-74.13468,9.148,latLng&t=2.73

## Slide 3
Papua New Guinea
Vegetation can affect floodplain deposition rates

## Slide 4
Vegetation is used to increase bank stability and aquatic habitat for river restoration

## Slide 5
Invasive vegetation can degrade natural channel conditions, particularly downstream of dams

## Slide 6: The influence of vegetation on sediment transport is not well understood

## Slide 7: Questions
How does vegetation affect flow and sediment transport?
How can we accurately predict bedload transport through vegetation?

## Slide 8: Experiments to determine the effects of vegetation on flow and sediment transport
1.3 cm

-hold mean flow velocity constant
-0.5 mm sand transported through regular cylinders
-scaled to field conditions in natural rivers
Flow
Notes: 4 minutes to here

## Slide 9: Vary the vegetation density between experiments
Vegetation density by area
0%
0.8%
1.7%
Flow
4.0%

## Slide 10
Particle imaging velocimetry records spatial and temporal variations in downstream and vertical velocities
Flow

## Slide 11
High-speed video records spatial and temporal variations in the sediment transport rate
Flow
Video camera

## Slide 13
Difference between images to obtain relative transport rates

## Slide 14
Calibrate each transport rate to individual counts of mobilized grains in videos

## Slide 15: Obtain detailed map of sediment transport rates around vegetation
Flow
Sediment transport rate (cm2/s)
0
0.02
0.002
0.09
0.04
0.08
Yager and Schmeeckle, 2013
Notes: 7 min to here

## Slide 16: For the same reach-averaged velocity: addition of vegetation increases spatial variation in the sediment transport rate
0%
Flow
Vegetation density by area
1.7%
Sediment transport rate (cm2/s)
0
0.02
0.002
0.09
0.04
0.08

## Slide 17: For the same reach-averaged velocity: addition of vegetation generally increases mean sediment transport rates
0%
Flow
Vegetation density by area
1.7%
Sediment transport rate (cm2/s)
0
0.02
0.002
0.09
0.04
0.08
Notes: 7 min to here

## Slide 18
Addition of vegetation increases turbulence
Flow
With vegetation
Without vegetation

## Slide 19: Addition of vegetation increases near-bed turbulence intensities, which can increase sediment transport
~2x
0.8%
1.7%
0%
4%
Yager and Schmeeckle, 2013
Notes: 11 min to this point

## Slide 20: Conclusions of indoor experiments
For a constant velocity, addition of rigid emergent vegetation increases:
turbulence intensities
sediment transport rates
Predicting sediment flux through vegetation patches will require some measure of turbulence

## Slide 21: Questions
How does vegetation affect flow and sediment transport?
How can we accurately predict bedload transport through vegetation?

## Slide 22
LES coupled with DEM would provide accurate predictions, but is computationally expensive and not currently practical for very large reaches or long-term landscape evolution
Mark Schmeeckle

## Slide 23
Luque and Van Beek equation (1976)
Total shear stress
Sediment transport rate
Critical shear stress
Use simple sediment transport equation to start

## Slide 24
Luque and Van Beek equation (1976)
Total shear stress
Sediment transport rate
Critical shear stress
Total shear stress does not account for effects of increased drag and turbulence
Notes: 24

## Slide 25
1:1
Order
of magnitude
Use of the total shear stress over-predicts sediment flux, as expected

## Slide 26
~ 5 mm
Luque and Van Beek equation (1976)
Near-bed Reynolds stress
Sediment transport rate
Critical shear stress
Use average near-bed Reynolds stress to account for vegetation induced drag and ~turbulence
-ru w

## Slide 27
1:1
Order
of magnitude
Use of the average Reynolds stress under-predicts sediment flux (11 points with 0 flux)
Average
Re stress
Total stress

## Slide 28
Stresses greater than the mean will cause much greater local sediment transport rates
Average near-bed Reynolds
stress=0.24 Pa

## Slide 29
1:1
Order
of magnitude
Use of the distribution of Reynolds stresses improves sediment flux predictions
Total stress
Distribution of
Re stress
Average
Re stress

## Slide 30
1:1
Order
of magnitude
Only 70% of predictions were within an order of magnitude of measured values
Total stress
Distribution of
Re stress
Average
Re stress

## Slide 31: Conclusions for flux predictions
Sediment transport equations need to account for:
- Spatial variation in stress (or velocity) and sediment flux around vegetation
Even with a spatial distribution of shear stress, bedload predictions are still not very accurate

## Slide 32: Questions
How does vegetation affect flow and sediment transport?
How can we accurately predict bedload transport through vegetation?

## Slide 33: Experiments-Outdoor Stream Lab
Hold stream discharge and sediment feed constant
Three different vegetation densities, two different arrangements (clustered and distributed)
Photo: Anne Lightbody

## Slide 34: Experiments-Outdoor Stream Lab
Hold stream discharge and sediment feed constant
Three different vegetation densities, two different arrangements (clustered and distributed)
Photo: Anne Lightbody
Hold stream discharge and upstream sediment supply approximately constant

## Slide 35: Experiments-Outdoor Stream Lab
Hold stream discharge and sediment feed constant
Three different vegetation densities, two different arrangements (clustered and distributed)
Photo: Anne Lightbody
Plant vegetation on point bar

## Slide 36: Vary vegetation frontal area (cm2)
4500
± 500
6000 ± 600
0

## Slide 37: Measure-near bed turbulence (3D) and sediment transport rates

## Slide 38
Measure bar topography and dune migration rates
Cross sections
Sonar scans of bar topography
Flow
Notes: 18 minutes to here

## Slide 39: Dune transport rates increased with greater vegetation frontal area

## Slide 40
Without vegetation and with distributed vegetation, sand dunes migrate over entire channel width
Flow

## Slide 41
With dense vegetation, dunes no longer migrate over bar and move faster over a smaller bed area
Flow

## Slide 42
With dense vegetation, dunes no longer migrate over bar and move faster over a smaller bed area
Flow
Same upstream supply

## Slide 43: Bedform transport rates>>bedload transport rates through vegetation
Bedforms
Bedload
(no bedforms)

## Slide 44: Lack of dune migration causes much lower transport through vegetation
Bedforms
Bedload
(no bedforms)

## Slide 45
Elevation change with clustered vegetation (mm)
Vegetation generally caused erosion of upstream end of bar
Outer bank
Inner bank
Flow

## Slide 46
Elevation change with clustered vegetation (mm)
Erosion likely due to lack of dune migration and enhanced turbulence at edge of vegetation patch
Flow

## Slide 47
Distinct scour holes developed immediately adjacent to the stems with areas of deposition downstream of stems
Flow

## Slide 48
Clustered vegetation may alter the near-bed turbulence and bedload transport patterns similarly to rigid simulated vegetation
Notes: 25 minutes

## Slide 49: Questions
How does vegetation affect flow and sediment transport?
How can we accurately predict bedload transport through vegetation?

## Slide 50: Use of distribution of near-bed velocities in bedload transport equation (Ackers and White) results in prediction of 0 flux through vegetation

## Slide 51: Use of distribution of near-bed velocities in bedload transport equation results in prediction of 0 flux through vegetation
Even with correct near-bed velocities or shear stresses (measured or predicted from numerical models), current bedload equations may not perform well in vegetation patches

## Slide 52: Develop simple bedload transport equation using rigid vegetation data: based on near-bed velocity, turbulence intensity and vegetation density
Predict mean flux through vegetation in OSL:
Measured bedload flux: 0.01 cm2/s
Predicted bedload flux: 0.015 cm2/s

## Slide 53: What is missing?
Bedload equations
developed for reach-
averaged, not local
conditions
Flow turbulence effects
are missing
Probabilistic equations
may perform better
But…larger –scale feedbacks between vegetation and bedform dynamics also must be considered.

## Slide 54: Conclusions from outdoor experiments
A dense and clustered arrangement of vegetation may significantly alter sediment transport processes by
halting bedform migration over the point bar top

## Slide 55: Conclusions from outdoor experiments
A dense and clustered arrangement of vegetation may significantly alter sediment transport processes by
halting bedform migration over the point bar top
increasing bedform transport rates at the outer bank
Bedforms
Bedload
(no bedforms)

## Slide 56: Conclusions from outdoor experiments
A dense and clustered arrangement of vegetation may significantly alter sediment transport processes by
halting bedform migration over the point bar top
increasing bedform transport rates at the outer bank
decreasing bedload transport rates on the point bar
Bedforms
Bedload
(no bedforms)

## Slide 57: Conclusions from outdoor experiments
A dense and clustered arrangement of vegetation may significantly alter sediment transport processes by
halting bedform migration over the point bar top
increasing bedform transport rates at the outer bank
decreasing bedload transport rates on the point bar
reducing point bar width
and elevation

## Slide 58
Test new eqn-first OSL description
6 near-bed velocities in vegetation
9 bedload samples

## Slide 60
Sediment flux=0.06+0.006log(velocity)+0.1a

## Slide 61
Test new eqn
Measured 0.01 cm2/s
Predicted 0.015
Ackers and White 0
Even when current eqns use actual near-bed flow conditions (or assuming these would be corrrectly predicted from 2D model/drag) current sediment transport equations do not perform well. Part of this is likely that these eqns:
Have been calibrated to mean flow conditions rather than near-bed conditions and therefore will underpredict because some assumption of drag may be implicit in coefficients etc. and therefore using mean actual bed flow will under-predict
Have not been developed for highly spatially variable flow and sediment transport conditions that occur around vegetation

## Slide 62: Add in the influence of flow hydrographs, which are more representative of natural conditions!

## Slide 63: Run each hydrograph with and without vegetation planted on bar

## Slide 64: Hydrograph shape influences bar form

## Slide 65: Vegetation combined with a flow hydrograph results in the formation of a side channel

## Slide 66: Side channel persists with more rapid hydrograph recession rate

## Slide 67: Such a side channel could provide habitat for fish but also could decrease bar stability