## Slide 1: Energy Balance and the Hydrological Cycle
Hydrology Lab
Posted by Irina Overeem, May 2016

## Slide 2: Importance of Energy Balance for Hydrological Cycle
Solar energy drives the global climate
Differential solar heating gives rise to an equator-to-pole temperature gradient, resulting in a gradient in the height of atmospheric pressure surfaces that drives the global atmospheric circulation.
Energy balance within a watershed varies dramatically with local slope and aspect

## Slide 3: Key Physical Concepts
Planetary Energy Balance – Stefan-Boltzmann Law
Radiant incident to horizontal plane - Cosine / Geometry
Impacts of watershed slope and aspect on incoming radiation

## Slide 4: Planetary Energy Balance
S= Solar energy Input
SHORT-WAVE
Reflected solar radiation = S (1-ap)
Stefan-Boltzmann Law
The total energy radiated per unit surface area of a black body per unit time is directly proportional to the fourth power of the black body's thermodynamic temperature T.
q= radiated heat from a black body
LONG-WAVE

## Slide 5: Planetary Energy Balance
S= 1.74 * 1017 W
Planetary albedo ~0.3
ap = 0.3
Stefan-Boltzmann Constant
σ = 5.67 *10-8 W m-2 K-4
Earth’s surface area
5.1 * 1014 m2
S= Solar energy Input
Planetary Temperature without Atmosphere
254 K (or -19C or -2F)
Notes: How would the mean temperature of the Earth change if its average albedo were changed to 0.1 or 0.5? (Courtesy Bob Anderson’s textbook, p 118).

## Slide 6: Greenhouse Gasses
Gasses like a.o. H2O, CO2, CH4,O2 absorb energy, mostly from emitted infrared light.
Temperature shift due to absorption makes Earth’s temperature warmer, to an average of 15°C.

## Slide 7: Earth’s Energy Balance and Greenhouse Gasses
Image Courtesy NASA (http://science-edu.larc.nasa.gov/energy_budget/)
Because of absorbtion and emission by greenhouse gases, most of the emission to space is from the atmosphere. Because of the counter-radiation back to the
surface from greenhouse gases (H20, CO2, CH4 and others) the earth’s average surface
temperature is a habitable 288 K, 33 K higher than the radiation emission temperature.

## Slide 8: Insolation: incoming Solar integrated over time
Image Courtesy Wikipedia
Annual average insolation at the top of the Atmosphere (TOA), depends on latitude
Annual average insolation at the top of land surface, depends on latitude, and on athmospheric reflectance and absorption (a.o. cloudiness).

## Slide 9: Radiation Incident on a Plane
η
equator
φ
Radiative Flux by latitude
Sij=cos(η+φ)
η = tilt of the Earth, varies -23.5° at summer soltice, to 23.5° at winter soltice.
φ = latitude
S0

## Slide 10: Hydrological Watershed
Watershed or drainage basin
Need to know its location: latitude and longitude.
Incoming radiation over the simulated events depends on the time of year.
Local morphometry of the watershed is important, because it further distributes the incoming energy.

## Slide 11: Morphometry of a Watershed
Aspect = direction that a topographical slope faces
North-facing slopes
South-facing slopes
Example in the alpine environment of the Rocky Mountains.
North-facing slopes hold snow and ice
for a longer period over the thaw cycle.
Image Courtesy; Irina Overeem

## Slide 12: Morphometry of a Watershed
Aspect = direction that a topographical slope faces
North-facing slopes
South-facing slopes
Example in Rocky Mountain region, near Salida, Colorado.
North-facing slopes hold moisture and promote woody vegetation, whereas south-facing slopes are more dry and only grasses and small shrubs can sustain.
Image Courtesy; Irina Overeem

## Slide 13: Beaver Creek Watershed, KY
Relief
Aspect
Classified into
45 degree bins
Beaver Creek is at 37° N

## Slide 14: WMT-Hydrology
Energy Balance in Meteorology Component
Select Meteorology Component
Save output for:
‘land-surface-net-shortwave-radiation__energy flux

## Slide 15: Setup in Meteorology
Use the example “Meteo_Shortwave_BeaverCreek”
Set up a run for a 6 hr simulation time (e.g. sunrise – noon) at an arbitrary date in the year.

## Slide 16: WMT Energy Balance examples

## Slide 17: WMT Energy Balance examples

## Slide 18: Exercises
Change the data settings to include the summer equinox, summer solstice
Can you discuss how short-wave radiation would change the Beaver Creek catchment would be at 70° N?
Show the implications of solar radiation differences with aspect.

## Slide 19: References
Dingman, S.L., 2008. Physical Hydrology, 2nd edition. ISBN 987-1-57766-561-8.
Anderson, R.S., Anderson, S., 2010. Geomorphology; the mechanics and chemistry of landscapes. ISBN 978-0-521-51978-6.