## Slide 1: Integrated Modeling Concepts
A clinic at the Community Surface Dynamics Modeling System (CSDMS) 2015 Annual Meeting
Boulder, Colorado
May 26-28, 2015
Jonathan Goodall
Associate Professor
Department of Civil and Environmental Engineering
University of Virginia
download slides: http://goo.gl/VRgzc9

## Slide 2: Clinic Aims
This clinic is intended for early career researchers interested in gaining an understanding of basic integrated modeling concepts as they relate to modeling earth science systems.
The class will present
  key literature in the field,
  core concepts and terminology, and
  different integrated modeling systems.
Past, present, and future trends for designing integrating modeling systems will be discussed.
Participants will also gain experience applying integrated modeling concepts using CSDMS for simplified integrated modeling examples.

## Slide 3: Outline
Introduction
  Motivation for integrated modeling/model coupling
  Terminology and key concepts
Example modeling frameworks
  CSDMS
  FRAMES
  ESMF
  OMS
  FluidEarth
Interface Standards
  OpenMI
  BMI
Current topics
  Semantics, ontologies, metadata controlled vocabularies
  Model web
Tutorials
  Getting Started with WMT (time permitting)
Summary

## Slide 4: Integrated Modeling Definition
“Integrated Modeling includes a set of interdependent science-based components (models, data, and assessment methods) that together form the basis for constructing an appropriate modeling system (EPA, 2008b, 2009).”
Source: Laniak et al., 2013

## Slide 5: Integrated Modeling Landscape
IM Applications: problem formations and solution approaches that are transparent and holistic; recognizing interdependent relationships
IM Science: transdisciplinary; human-environmental systems; stresses model uncertainties
IM Technology: provide a means to express, integrate, and share the science of IEM; standards and tools to facilitate the discovery, access, and integration of science components.
A Community of IEM stakeholders and associated organizations
Source: Laniak et al., 2013
The primary focus of this talk will be on the technology aspects of IM

## Slide 6: Example of Integrated Modeling
Source: Liu et al., 2008

## Slide 7: The big picture workflow
Source: Liu et al., 2008

## Slide 9: Argent (2004) Model Integration at development and application levels I-IV
Source: Argent, 2004
Models developed by individuals for a specific research purpose
More general models that can be used for a range of research purposes
Flexible application to a range of situations; operations ready
Modelers not familiar with model workings; model operates as black box

## Slide 10: Two views of model integration
Source: Argent, 2004
File-based
In-memory

## Slide 11: Terminology and Key Concepts
Development environment – a place where components can be built based upon existing components or component templates
Core components – a library of components that represent various pieces of knowledge
Support components – a library of components for common tasks (e.g., data collection, gap filling, basic analysis, output, and visualization).
Modeling framework – the place where modelers construct and manipulate multi-component models.
Integrated documentation system – for managing components and their metadata
Resource discovery system – for identification and access of components
Model execution system – supports model runs potentially in parallel from multiple users.
Source: Argent, 2004

## Slide 12: Argent’s final paragraph is still true today …
Source: Argent, 2004

## Slide 13: What are these semantic issues?
“the meaning of data, variable and parameter names that are loaded into, used by, or exchanged between, components.”
“misunderstandings will arise unless there is a clear and established meaning for various state variables and concepts, and an agreed language for communicating these.”
Source: Argent, 2004

## Slide 14: Argent’s prediction for progress in semantic issues
First, we need to acknowledge that these semantic difficulties exist and that the difficulties will be expanded as the scope of integrated modeling expands
Then, “as we gain experience in working with and explaining our terminology to members of other disciplines, we will develop a more semantically rich language”
Argent, 2004

## Slide 15: Outline
Introduction
  Motivation for integrated modeling/model coupling
  Terminology and key concepts
Example modeling frameworks
  CSDMS
  FRAMES
  ESMF
  OMS
  FluidEarth
Interface Standards
  OpenMI
  BMI
Current topics
  Semantics, ontologies, metadata controlled vocabularies
  Model web
Tutorials (time permitting)
  Getting Started with WMT
Summary

## Slide 16: CSDMS Architecture
Source: Peckham et al., 2013

## Slide 17: Original CSDSM Modeling Tool (replaced by by Web Modeling Tool: WMT)
Source: Peckham et al., 2013

## Slide 18: CSDMS Web Modeling Tool (WMT)

## Slide 19: EPA FRAMES
Whelan et al., 2014

## Slide 20: EPA FRAMES Module Editor
Whelan et al., 2014

## Slide 21: Frames Dictionary Editor
Whelan et al., 2014

## Slide 22: Frames Unit Conversation Editor
Whelan et al., 2014

## Slide 23: FRAMES Domain Editor
Whelan et al., 2014

## Slide 24: FRAMES Simulation Editor
Whelan et al., 2014

## Slide 25: ESMF
Earth System Modeling Framework
Global models
HPC emphasis
Coupling models with gridded data structures
Source: Hill et al., 2004

## Slide 26: Components and Couplers in ESMF

## Slide 27: Some of the ESMF Benefits
Well tested and used in operations
Optimized to reduce overhead due to coupling in high performance computing (HPC) environments
Parallel regridder with Python bindings that can be used apart from ESMF (e.g., it is used by CSDMS)

## Slide 28: Object Modeling System 3 (OMS3)
http://www.javaforge.com/project/oms

## Slide 29: Object Modeling System 3 (OMS3): Principle Framework Architecture
Source: David et al., 2013

## Slide 30: OMS3 Component Architecture
Source: David et al., 2013

## Slide 31: Example hydrologic model implemented as components in OMS3
Source: David et al., 2013

## Slide 32: FluidEarth
FluidEarth is a functional and technical platform for using OpenMI.
eInfrastructure http://fluidearth.net http://catalogue.fluidearth.net http://sourceforge.net/projects/fluidearth/
Tools Fluid Earth SDK Pipistrelle GUI (Reference Implementations for OpenMI 2.0)
Models A library of models available for compositions
Community Model providers and users
Source: HR Wallingford, fluidearth.net

## Slide 33: The FluidEarth Toolkit: Pipistrelle & SDK
The FluidEarth Software Development Kit is an OpenMI API:
- Creation of OpenMI 2.0 in C#, VB and FORTRAN; - Windows or Linux (under Mono); - Available on SourceForge in “Fluid Earth” project.
Pipistrelle is a tool for running OpenMI compositions:
- OpenMI 2.0; - Windows (with GUI) or Linux (under Mono, with console only); - Adaptor functionality; - Component Builder Plug-in (initial version); - Compatibility with and conversion of FE OpenMI 1.4 components into FE OpenMI 2.0 components to follow (if Data Operations not used);
- Spatial View Plug-in (to follow); - Available on Source Forge in “Fluid Earth” project.
Source: HR Wallingford, fluidearth.net

## Slide 34: 2-way Connection
.omi
.xml
Configuration
Model Engine 1
In
Out
Complete
Configuration
.omi
.xml
Model Engine 2
Perform
Timestep
Initialize
Initialize
Complete
Perform
Timestep
TRIGGER
In
ADAPTOR
Out
Source: HR Wallingford, fluidearth.net

## Slide 35: Outline
Introduction
  Motivation for integrated modeling/model coupling
  Terminology and key concepts
Example modeling frameworks
  CSDMS
  FRAMES
  ESMF
  OMS
  FluidEarth
Interface Standards
  OpenMI
  BMI
Current topics
  Semantics, ontologies, metadata controlled vocabularies
  Model web
Tutorials (time permitting)
  Getting Started with WMT
Summary

## Slide 36: Run-time Coupling between Model Engines
Source: Moore and Tindall, 2005

## Slide 37: Refactoring Model to IRF Paradigm
Source: Moore and Tindall, 2005

## Slide 38: Manual Semantic Mediation
Source: Moore and Tindall, 2005

## Slide 39: Spatial Referencing of Model Data Exchanges
Source: Moore and Tindall, 2005

## Slide 40: Data model for exchanges between models
Source: Moore and Tindall, 2005

## Slide 41: UML View of Quantities in OpenMI
Source: Moore and Tindall, 2005

## Slide 42: Links are used to define data exchanges between model components within a specific model configuration
Source: Moore and Tindall, 2005

## Slide 43: “request and reply” mechanism for data exchanges
Source: Moore and Tindall, 2005

## Slide 44: Components implement the ILinkableComponent Interface
Source: Moore and Tindall, 2005

## Slide 45: OpenMI 2.0 changes how models are linked
OpenMI version 1.4 uses data operations on links as discussed before
OpenMI version 2.0 uses the concept of data adaptors
Source: document #11-014r3 available here: http://www.opengeospatial.org/standards/openmi

## Slide 46: Basic Modeling Interface (BMI)
BMI is defined using the Scientific Interface Description Lanaguage (SIDL) here: https://github.com/csdms/bmi/blob/master/bmi.sidl
BMI is meant to be a light-weight (basic) interface for exposing models as components
Frameworks would wrap BMI components using framework-specific model interface standards
<interface>
bmi
+ initialize()
+ update()
+ finalize()
+ get_start_time()
+ get_current_time()
+ get_end_time()
+ get_component_name()
+ get_input_var_names()
+ get_output_var_names()
+ get_value()
+ set_value()
+ get_var_units()
+ get_var_type()
+ get_var_grid()
+ get_grid_spacing()
+ get_grid_origin()
+ get_grid_shape()

## Slide 47: Proposed BMI to OpenMI Architecture
BMI Component 1
BMI Component 2
BMI Component N
BMI .Net Wrapper
BMI to OpenMI Bridge Wrapper
...
OpenMI Framework 1
OpenMI Framework 2
OpenMI Framework N
...
BMI-compliant model components written in Python, C, or Fortran
Two layers of wrappers for (1) C# .NET interoperability and (2) BMI to OpenMI bridging
BMI components can be used in OpenMI v2.0 compliant frameworks such as FluidEarth

## Slide 48
<interface>
bmi
+ initialize()
+ update()
+ finalize()
+ get_start_time()
+ get_current_time()
+ get_end_time()
+ get_component_name()
+ get_input_var_names()
+ get_output_var_names()
+ get_value()
+ set_value()
+ get_var_units()
+ get_var_type()
+ get_var_grid()
+ get_grid_spacing()
+ get_grid_origin()
+ get_grid_shape()
<interface>
ITimeSpaceComponent
<interface>
IBaseLinkableComponent
+ Initialize()
+ Update()
+ Finish()
<<attributes>>
+ Arguments : IList<Argument>
+ Inputs : IList<ITimeSpaceInput>
+ Outputs :IList<ITimeSpaceOutput>
<interface>
ITimeSpaceExchangeItem
<interface>
IBaseExchangeItem
<<attributes>>
+ Component : IBaseLinkableComponent
+ ValueDefinition : IValueDefinition
<<attributes>>
+ SpatialDefinition : ISpatialDefinition
+ TimeSet : ITimeSet
<interface>
ITimeSpaceOutput
+ GetValues() : ITimeSpaceValueSet
<<attributes>>
+ Values : ITimeSpaceValueSet
Key Interfaces in BMI and OpenMI
bmi
OpenMI 2.0

## Slide 49: Mapping between BMI and OpenMI 2.0
This will be presented for 5 categories using the following color coding convention:
Initialize, Run, Finalize (IRF) methods
General metadata properties
Getters and setters
Time information
Spatial representations

## Slide 50: Overview of Mapping From BMI to OpenMI
<interface>
bmi
+ initialize()
+ update()
+ finalize()
+ get_start_time()
+ get_current_time()
+ get_end_time()
+ get_component_name()
+ get_input_var_names()
+ get_output_var_names()
+ get_value()
+ set_value()
+ get_var_units()
+ get_var_type()
+ get_var_grid()
+ get_grid_spacing()
+ get_grid_origin()
+ get_grid_shape()
<interface>
ITimeSpaceComponent
<interface>
IBaseLinkableComponent
+ Initialize()
+ Update()
+ Finish()
<<attributes>>
+ Arguments : IList<Argument>
+ Inputs : IList<ITimeSpaceInput>
+ Outputs :IList<ITimeSpaceOutput>
Due to space restrictions, only selected information shown.
<interface>
ITimeSpaceExchangeItem
<interface>
IBaseExchangeItem
<<attributes>>
+ Component : IBaseLinkableComponent
+ ValueDefinition : IValueDefinition
<<attributes>>
+ SpatialDefinition : ISpatialDefinition
+ TimeSet : ITimeSet
<interface>
ITimeSpaceOutput
+ GetValues() : ITimeSpaceValueSet
<<attributes>>
+ Values : ITimeSpaceValueSet
bmi
OpenMI 2.0

## Slide 51: Outline
Introduction
  Motivation for integrated modeling/model coupling
  Terminology and key concepts
Example modeling frameworks
  CSDMS
  FRAMES
  ESMF
  OMS
  FluidEarth
Interface Standards
  OpenMI
  BMI
Current research topics
  Semantics, ontologies, metadata controlled vocabularies
  Model web
Tutorials
  Getting Started with WMT
Summary

## Slide 52: Semantics: From Glossaries to Ontologies
Villa et al., 2009

## Slide 53: Example of Semantic Annotation for a Model Input
Villa et al., 2009

## Slide 54: Sematic Relationships within Models
Villa et al., 2009

## Slide 55: Semantic Matching for Model Variables
Hydro Model A
Output variables:
streamflow
rainrate
Hydro Model B
Input variables:
discharge
precip_rate
CSDMS Standard Names
channel_exit_water_x-section__
volume_flow_rate
atmosphere_water__rainfall_volume_flux
Goal: Remove ambiguity so that
the framework can automatically
match outputs to inputs.
Peckham, 2014

## Slide 56: HydroShare
NSF supported collaborative project building from the CUAHSI Hydrologic Information System (HIS) project
Resource-based sharing of hydrologic data, models, analysis tools, etc.
Share resources with metadata with collaborators or public
Discover resources use hydrology-specific metadata
Social objects (comments, rating, etc.)
http://beta.hydroshare.org is live now and http://www.hydroshare.org is coming soon (the plan is for this summer)

## Slide 57: Conceptualization of Key Model Concepts and Relationships: Component-based Modeling
Morsy et al., 2014

## Slide 58: Conceptualization of Key Model Concepts and Relationships: Stand-alone Models
Morsy et al., 2014

## Slide 59
Morsy et al., 2014
Model Metadata: Capturing Connections Between Models, Components, Raw Data, Derived Data, Model Inputs, Model Outputs, Developers, Users, Modeling Objectives, Etc.

## Slide 60
Nativi et al., 2013

## Slide 61
Nativi et al., 2013

## Slide 62: OMS 3 within the Cloud Services Innovation Platform architecture
David et al., 2013

## Slide 63: The Model Resource Data Model proposed by Nativi et al. (2013)
Nativi et al., 2013

## Slide 64: Example of using model web concept for coupling earth system models
Goodall et al., 2013

## Slide 65: OpenMI/ESMF Interoperability via Web Services
Goodall et al., 2013

## Slide 66: Data flow for OpenMI/ESMF Interoperability
Goodall et al., 2013

## Slide 67: Scaling analysis: Data transmission time vs. model execution time
Goodall et al., 2013

## Slide 68: Modeling Web using REST/ OGC Web Processing Service
Models exposed as services using the Open Geospatial Consortium (OGC) Web Processing Service (WPS) standard.
Get Capabilities gives metadata about models on server
Describe Process gives metadata about a specific model service
Execute is more complex that a typical WPS to support model time stepping (e.g., session state with users must be maintained)
Castonova et al., 2013

## Slide 69: Outline
Introduction
  Motivation for integrated modeling/model coupling
  Terminology and key concepts
Example modeling frameworks
  CSDMS
  FRAMES
  ESMF
  OMS
  FluidEarth
Interface Standards
  OpenMI
  BMI
Current topics
  Semantics, ontologies, metadata controlled vocabularies
  Model web
Tutorials (time permitting)
  Getting Started with WMT
Summary

## Slide 70: WMT Tutorial
Time permitting, I will briefly show how integrated modeling concepts are used by the CSDMS WMT.
I will use the integrated model described in the coastal evolution lab available here: https://csdms.colorado.edu/wiki/Labs_WMT_CEM

## Slide 71: Outline
Introduction
  Motivation for integrated modeling/model coupling
  Terminology and key concepts
Example modeling frameworks
  CSDMS
  FRAMES
  ESMF
  OMS
  FluidEarth
Interface Standards
  OpenMI
  BMI
Current topics
  Semantics, ontologies, metadata controlled vocabularies
  Model web
Tutorials (time permitting)
  Getting Started with WMT
Summary

## Slide 72: Take home points
What is integrated modeling? IM seeks to provide methods and tools that allow for the combination of data, models, assessment methods from multiple disciplines into a single simulation system.
How is this typically accomplished now? By defining modular components (or services) that encapsulate disciplinary knowledge and then coupling components using a modeling framework to simulate a system.
What are some key challenges that require attention by researchers? Creating general interface standards and semantic mediation across disciplines are two key challenges.
Where is this all heading? To a model web: Both web-based configuration of HPC models and Models as Services. Why? To overcome hardware and software dependencies; to advance reproducible, reusable, and extensible of models; to take advance of cloud infrastructures.

## Slide 73: References (1 of 2)
Argent, R.M., 2004. An overview of model integration for environmental applications - Components, frameworks and semantics. Environ. Model. Softw. 19, 219–234. doi:10.1016/S1364-8152(03)00150-6
Boettiger, C., 2015. An introduction to Docker for reproducible research. ACM SIGOPS Oper. Syst. Rev. 49, 71–79. doi:10.1145/2723872.2723882
Castronova, A.M., Goodall, J.L., Ercan, M.B., 2013. Integrated modeling within a Hydrologic Information System: An OpenMI based approach. Environ. Model. Softw. 39, 263–273. doi:10.1016/j.envsoft.2012.02.011
David, O., Ascough, J.C., Lloyd, W., Green, T.R., Rojas, K.W., Leavesley, G.H., Ahuja, L.R., 2013. A software engineering perspective on environmental modeling framework design: The Object Modeling System. Environ. Model. Softw. 39, 201–213. doi:10.1016/j.envsoft.2012.03.006
Elag, M.M., Goodall, J.L., Castronova, A.M., 2011. Feedback loops and temporal misalignment in component-based hydrologic modeling. Water Resour. Res. 47, n/a–n/a. doi:10.1029/2011WR010792
Goodall, J.L., Saint, K.D., Ercan, M.B., Briley, L.J., Murphy, S., You, H., DeLuca, C., Rood, R.B., 2013. Coupling climate and hydrological models: Interoperability through Web Services. Environ. Model. Softw. 46, 250–259. doi:10.1016/j.envsoft.2013.03.019
Gregersen, J.B., Gijsbers, P.J.A., Westen, S.J.P., 2007. OpenMI: Open modelling interface. J. Hydroinformatics 9, 175. doi:10.2166/hydro.2007.023
Hill, C., DeLuca, C., Suarez, M., Da Silva, A., 2004. The architecture of the earth system modeling framework. Comput. Sci. Eng. 6, 18–28. doi:10.1109/MCISE.2004.1255817
Laniak, G.F., Olchin, G., Goodall, J.L., Voinov, A., Hill, M., Glynn, P., Whelan, G., Geller, G., Quinn, N., Blind, M., Peckham, S., Reaney, S., Gaber, N., Kennedy, R., Hughes, A., 2013. Integrated environmental modeling: A vision and roadmap for the future. Environ. Model. Softw. 39, 3–23. doi:10.1016/j.envsoft.2012.09.006

## Slide 74: References (2 of 2)
Liu, Y., Gupta, H., Springer, E., Wagener, T., 2008. Linking science with environmental decision making: Experiences from an integrated modeling approach to supporting sustainable water resources management. Environ. Model. Softw. 23, 846–858. doi:10.1016/j.envsoft.2007.10.007
Moore, R. V., Tindall, C.I., 2005. An overview of the open modelling interface and environment (the OpenMI). Environ. Sci. Policy 8, 279–286. doi:10.1016/j.envsci.2005.03.009
Morsy, M.M., Goodall, J.L., Bandaragoda, C., Castronova, A.M., Greenberg, J., 2014. Metadata for Describing Water Models, in: International Environmental Modelling and Software Society (iEMSs) 7th International Congress on Environmental Modelling and Software. doi:10.13140/2.1.1314.6561
Nativi, S., Mazzetti, P., Geller, G.N., 2013. Environmental model access and interoperability: The GEO Model Web initiative. Environ. Model. Softw. 39, 214–228. doi:10.1016/j.envsoft.2012.03.007
Peckham, S.D., 2014. The CSDMS Standard Names: Cross-Domain Naming Conventions for Describing Process Models, Data Sets and Their Associated Variables. Int. Environ. Model. Softw. Soc. (iEMSs), San Diego, California, USA.
Peckham, S.D., Hutton, E.W.H., Norris, B., 2013. A component-based approach to integrated modeling in the geosciences: The design of CSDMS. Comput. Geosci. 53, 3–12. doi:10.1016/j.cageo.2012.04.002
Villa, F., Athanasiadis, I.N., Rizzoli, A.E., 2009. Modelling with knowledge: A review of emerging semantic approaches to environmental modelling. Environ. Model. Softw. 24, 577–587. doi:10.1016/j.envsoft.2008.09.009
Whelan, G., Kim, K., Pelton, M.A., Castleton, K.J., Laniak, G.F., Wolfe, K., Parmar, R., Babendreier, J., Galvin, M., 2014. Design of a component-based integrated environmental modeling framework. Environ. Model. Softw. 55, 1–24. doi:10.1016/j.envsoft.2014.01.016

## Slide 75: Acknowledgements
Support for the development of this clinic material was provided by the National Science Foundation under award number CBET-0846244.

## Slide 76: Questions?
Contact info:
Jon Goodall
University of Virginia
Dept. of Civil and Environmental Engineering
goodall@virginia.edu
download slides: http://goo.gl/VRgzc9