## Slide 1
A Simple Model for Oxygen Dynamics in Chesapeake Bay
Malcolm Scully
Background and Motivation
Simplified Modeling Approach
Importance of Physical Forcing to Seasonal Variations in Hypoxic Volume
  River Discharge
  Heat Flux / Temperature
  Wind (Magnitude and Direction)
Inter-annual Variation in Hypoxic Volume
Conclusions
Center for Coastal Physical Oceanography
Old Dominion University
Center for Coastal Physical Oceanography
Community Surface Dynamics Modeling System (CSDMS)
2011 Meeting; Boulder, CO
Outline:

## Slide 2
Testbed to Improve Models of Environmental Processes on the U.S. Atlantic and Gulf of Mexico Coasts
Estuarine Hypoxia Team
Federal partners
David Green (NOAA-NWS) – Transition to operations at NWS
Lyon Lanerole, Rich Patchen, Frank Aikman (NOAA-CSDL) – Transition to operations at CSDL; CBOFS2
Lewis Linker (EPA), Carl Cerco (USACE) – Transition to operations at EPA; CH3D, CE-ICM
Doug Wilson (NOAA-NCBO) – Integration w/observing systems at NCBO/IOOS
CSDMS partners
Carl Friedrichs (VIMS) – Project Coordinator
Marjorie Friedrichs, Aaron Bever (VIMS) – Metric development and model skill assessment
Ming Li, Yun Li (UMCES) – UMCES-ROMS hydrodynamic model
Wen Long, Raleigh Hood (UMCES) – ChesROMS with NPZD water quality model
Scott Peckham, Jisamma Kallumadikal (UC-Boulder) – Running multiple models on a single HPC cluster
Malcolm Scully (ODU) – ChesROMS with 1 term oxygen respiration model
Kevin Sellner (CRC) – Academic-agency liason; facilitator for model comparison
Jian Shen (VIMS) – SELFE, FVCOM, EFDC models

## Slide 3
1) Run CSDMS Modeling Tool
2) “File”  “Open Project”
 “Marine”  “ROMS”
3) Drag selected “Palette”
(“chesROMS” in this case)
into Driver;
4) Choose “Configure”, adjust
settings as desired;
5) Run chesROMS
ChesROMS and two other flavors of ROMS are already incorporated into CSDMS.

## Slide 4
From Chesapeake Bay Program newsletter: http://ian.umces.edu/pdfs/do_letter.pdf
Map of Mean Bottom Dissolved Oxygen -- Summer 2005
Low DO has significant impact on a wide array of biological and ecological processes.
Large regions of Chesapeake Bay are impacted by hypoxia/anoxia.
Over $ 3.5 billion was spent on nutrient controls in Chesapeake Bay between 1985-1996 (Butt & Brown, 2000)
Assessing success/failure of reductions in nutrient loading requires understanding of the physical processes that contribute to the inter-annual variability.

## Slide 6
Regional Ocean Modeling System (ROMS)
ChesROMS Model Grid
Model forcing
Realistic tidal and sub-tidal elevation at ocean boundary
Realistic surface fluxes from NCEP (heating and winds)
Observed river discharge for all tributaries.
Temperature and salinity at ocean boundary from World Ocean Atlas.

## Slide 7
Oxygen Model
Oxygen is introduced as an additional model tracer.
Oxygen consumption (respiration) is constant in time, with depth-dependent vertical distribution.
No oxygen consumption outside of estuarine portion of model
No oxygen production.
Open boundaries = saturation
Surface flux using wind speed dependent piston velocity following Marino and Howarth, 1993.
No negative oxygen concentration and no super-saturation.
Depth-dependent Respiration Formulation
Surface Oxygen Flux using Piston Velocity:
From Marino and Howarth, Estuaries, 1993
Model assumes biology is constant so that the role of physical processes can be isolated!

## Slide 8
Seasonal and Inter-Annual Variability in Hypoxic Volume (from CBP data 1984-2009)
Maximum observed
Minimum observed
Data compiled from Murphy et al. (submitted)

## Slide 9
Variability of Physical Forcing
What is relative importance of different physical forcing in controlling seasonal and inter-annual variability of hypoxia in Chesapeake Bay?

## Slide 10
Comparison with Bottom DO at Chesapeake Bay Program Stations

## Slide 11
July 19-21, 2004
August 9-11, 2004
Comparison with Chesapeake Bay Program Data
Bottom Dissolved Oxygen Concentration (mg/L)

## Slide 12
In addition to seasonal cycle, model captures some of the inter-annual variability
485 km3days
476 km3days
707 km3days
Model predicts roughly 50% more hypoxia in 2004 than in 2005, solely due to physical variability.

## Slide 13
Physical Controls on Hypoxia in Chesapeake Bay
Malcolm Scully
Background and Motivation
Simplified Modeling Approach
Importance of Physical Forcing to Seasonal Variations in Hypoxic Volume
  River Discharge
  Heat Flux / Temperature
  Wind (Magnitude and Direction)
Inter-annual Variation in Hypoxic Volume
Conclusions
Center for Coastal Physical Oceanography
Old Dominion University
Center for Coastal Physical Oceanography
Virginia Institute of Marine Sciences, Seminar
October 21, 2011
Outline:

## Slide 14
River Discharge Monthly Climatology
Month
m3/s
Susquehanna River at Conowingo Dam (1967-2010)

## Slide 15
2004
Hypoxic Volume (< 1 mg/L)
Importance of Seasonal Variations in River Flow

## Slide 16
Sensitivity to River Discharge
469 km3days
488 km3days
476 km3days
423 km3days
Integrated volumes:
2004
Hypoxic Volume (< 1 mg/L)
Order of magnitude change in river discharge leads to less than 10% change in integrated hypoxic volume.

## Slide 17
Water Temperature
Monthly climatology at Thomas Point Light (1986-2009)

## Slide 18
Importance of Seasonal Variations in Temperature

## Slide 19
To simulate realistic variability in temperature forcing, model was run changing the air temperature by ± one standard deviation based on monthly climatology for air temperature.
Bay-averaged Water Temp (model)
Thomas Point Light Water Temp
1992
1998
+ 1 std air temp
- 1 std air temp

## Slide 20
Sensitivity to Temperature
421km3days
534 km3days
Integrated volumes:
2004
Hypoxic Volume (< 1 mg/L)
Increase in surface heating results in greater than 20% change in integrated hypoxic volume.
+ 1 std air temp
- 1 std air temp

## Slide 21
Wind Climatology from Thomas Point Light (1986-2010)
a) Wind Speed
b) Wind Direction
Wind Forcing
m/s

## Slide 22
Importance of Seasonal Variations in Wind
2004
Hypoxic Volume (< 1 mg/L)

## Slide 23
Average Monthly Wind Speed from Model Mid-Bay location
To simulate realistic variability in wind forcing, May-August wind magnitudes were increased/decreased by 15%.

## Slide 24
Sensitivity to Wind Speed
751 km3days
476 km3days
242 km3days
Integrated volumes:
2004
Hypoxic Volume (< 1 mg/L)
Realistic changes in summer wind speed could change hypoxic volume by a factor of 3

## Slide 25
Base Summer Winds
Positive 90°
Negative 90°
180°
Sensitivity to Summer Wind Direction
Modeled summer wind direction

## Slide 26
Sensitivity to Summer Wind Direction
548 km3days
527 km3days
476 km3days
278 km3days
Integrated volumes:
2004
Hypoxic Volume (< 1 mg/L)
Changes in wind direction can change the hypoxic volume by a factor of 2

## Slide 27
Physical Controls on Hypoxia in Chesapeake Bay
Malcolm Scully
Background and Motivation
Simplified Modeling Approach
Importance of Physical Forcing to Seasonal Variations in Hypoxic Volume
  River Discharge
  Heat Flux / Temperature
  Wind (Magnitude and Direction)
Inter-annual Variation in Hypoxic Volume
Conclusions
Center for Coastal Physical Oceanography
Old Dominion University
Center for Coastal Physical Oceanography
Virginia Institute of Marine Sciences, Seminar
October 21, 2011
Outline:

## Slide 28
15-year Simulations (1991-2005)

## Slide 29
Observations
Model
Hypoxic Volume (<1mg/L)
Hypoxic Volume (<1mg/L)
max
min
mean
month
month
Analysis of 15-year Simulation of Hypoxic Volume (1991-2005)
Model with no biologic variability shows significant inter-annual variability
Observations have greater variability than model
Model under predicts in early summer and slightly over predicts in late summer
Bi-monthly Averages

## Slide 30
Does variation in physical forcing explain observed inter-annual variability in hypoxic volume?
Annual Mean Hypoxic Volume (Observed)
Annual Mean Hypoxic Volume (Modeled)
r = 0.32
p = 0.25
Not in a statistically significant way!

## Slide 31
Next Steps: Simplified Load-Dependent Respiration Rate
Monthly-averaged Respiration Rate
Load-Dependent Respiration Rate (Scaled by Integrated Nitrogen Loading—Previous 250 days)

## Slide 32
Preliminary Results with Load-Dependent Respiration Rate
Hypoxic Volume (Observed)
Hypoxic Volume (Modeled)
Hypoxic Volume (Observed)
Hypoxic Volume (Modeled)
Constant Resp. Rate
Load-dependent Resp. Rate
r = 0.628
p =0.016
r = 0.315
p =0.252

## Slide 33
Conclusions
A relatively simple model with no biological variability can reasonably account for the seasonal cycle of hypoxia in Chesapeake Bay.
Wind speed and direction are the two most important physical variables controlling hypoxia in the Bay.
Model results are largely insensitive to variations in river discharge, when the role of nutrient delivery is not accounted for.
Changes in air temperature and the associated changes in water temperature via sensible heat flux can have a measurable influence on the overall hypoxic volume.
A 15-year model simulation with constant respiration rate produces significant inter-annual variability in hypoxic volume, by largely fails to reproduce the observed variability.
Model residuals are significantly correlated with the integrated Nitrogen loading demonstrating the importance of biological processes in controlling inter-annual variability
Preliminary attempts to include the effects of nutrient loading though a load-dependent respiration formulation show promise for capturing observed inter-annual variability.